## Slide 1: Digital Logic
Juan Chen
University of Electronic Science and Technology of China

## Slide 2: QQ Group for Our Course
Please change your nickname as: your real name + student number

## Slide 3: Grading Policy
Final Exam: 40%
Usual Performance: 60%

## Slide 4: SPOC: online learning resource
https://www.icourse163.org/spoc/course/UESTC-1462160180
Password：DigitalLogic

## Slide 5: Log In SPOC
Verify your account and register SPOC

## Slide 7: In this course you will study:
How is the computer working?
This course is all about numbers, functions and logic circuits.

## Slide 8: Tour of Digital Logic
2nd Tour:
Logic Functions
3rd Tour:
Logic Circuits
1st Tour:
Number Systems

## Slide 9: Tour of Digital Logic
(110011010100)2
(110 011 010 100)2: octal number (6324)8
1st Tour:
Number Systems
decimal number (3284)10
(1100 1101 0100)2: hex number (CD4)16
(?)10(?)2(?)8(?)16

## Slide 10: Tour of Digital Logic
1: ON, 0: OFF
X1, …, Xn: input
2nd Tour:
Logic Functions
Y1, …, Ym: output
Yj = f (X1, …, Xn), f: logic function
10001001…000111: X1, …, Xn
11110011…100010: Y1, …, Ym

## Slide 11: Tour of Digital Logic
Numbers
(Information)
Functions
(Operations)
Job for Computer
(e.g. Chatting)
What’s the weather today?
Robot: Sunny.

## Slide 12: Tour of Digital Logic
3rd Tour:
Logic Circuits
Hardware Implementation: CMOS Transistors
Software Simulation: Verilog
Industrial Product: Memory, Programmable Logic Device
How to demonstrate the job result?

## Slide 13
Chapter One: Number Systems and Codes
Chapter Two: Logical Algebra
Chapter Three: Digital Circuit
Chapter Four: Combinational Logic Circuit
Chapter Five: Flip-Flop
Chapter Six: Synchronous Sequential Logic Circuit
Chapter Seven: Verilog Implementation of Logic Circuit
Chapter Eight: Memory and Programmable Logic Device
Course Chapters

## Slide 14
Textbook
Digital Design: Principles and Practices
(4th Edition),
John F. Wakerly,
Pearson,
2005.

## Slide 15: Chapter One: Number Systems and Codes

## Slide 16
Chapter 1
1.1 Number Systems
1.2 Number Conversion
1.3 Signed Binary Numbers
1.5 Numerical Codes
Number Systems and Codes
1.4 Addition and Subtraction of Signed Binary Numbers

## Slide 17: 1.1 Number Systems
(1) Base: 10, Counting Symbols: 0～9
(2) Weight for the ith digit: 10i
1.1.1 Decimal Number (Base 10)
Weighted Expansion (m integers, n fractional digits):
Notes: Decimal number. The base is 10. It counts from 0 to 9. Alpha is the counting symbol.
For integers, the exponent starts from 0 and is increased by 1.
For decimals, the exponent starts from -1 and is decreased by 1.

## Slide 18: 1.1 Number Systems
(1) Base: 10, Counting Symbols: 0～9
(2) Weight for the ith digit: 10i
1.1.1 Decimal Number (Base 10)
Weighted Expansion (m integers, n fractional digits):
Notes: Decimal number. The base is 10. It counts from 0 to 9. Alpha is the counting symbol.
For integers, the exponent starts from 0 and is increased by 1.
For decimals, the exponent starts from -1 and is decreased by 1.

## Slide 19
How to write the weighted expansion of a decimal number ?
Example:
256.7
=2×102＋5×101＋6×100＋7×10－1
Notes: Look at the decimal number 256.7.
The base is 10.
For integers, the exponent starts from 0.
For decimals, the exponent starts from -1.

## Slide 20
(1) Base: 2, Counting Symbols: 0～1
(2) Weight for the ith digit: 2i
1.1.2 Binary Number (Base 2)
Weighted Expansion (m integers, n fractional digits):

## Slide 21
(1) Base: 2, Counting Symbols: 0～1
(2) Weight for the ith digit: 2i
1.1.2 Binary Number (Base 2)
Weighted Expansion (m integers, n fractional digits):

## Slide 22
How to write the weighted expansion of a binary number ?
Example:
(101.1)2
=1×22＋0×21＋1×20＋1×2-1
=(5.5)10

## Slide 23
(1) Base: 8, Counting Symbols: 0～7
(2) Weight for the ith digit: 8i
1.1.3 Octal Number (Base 8)
Weighted Expansion (m integers, n fractional digits):

## Slide 24
(1) Base: 8, Counting Symbols: 0～7
(2) Weight for the ith digit: 8i
1.1.3 Octal Number (Base 8)
Weighted Expansion (m integers, n fractional digits):

## Slide 25
How to write the weighted expansion of an octal number ?
Example:
(12.4)8
=1×81＋2×80＋4×8－1
=(10.5)10

## Slide 26
Decimal
Number
Hexadecimal
Number
10
11
12
13
14
15
A
B
C
D
E
F
Binary
Number
1010
1011
1100
1101
1110
1111
Weights
8 4 2 1
= 23 22 21 20

## Slide 27
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
(1) Base: 16, Counting Symbols: 0～F
(2) Weight for the ith digit: 16i
Weighted Expansion (m integers, n fractional digits):
1.1.4 Hexadecimal Number (Base 16)

## Slide 28
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
(1) Base: 16, Counting Symbols: 0～F
(2) Weight for the ith digit: 16i
Weighted Expansion (m integers, n fractional digits):
1.1.4 Hexadecimal Number (Base 16)

## Slide 29
How to write the weighted expansion of a hexadecimal number ?
e.g.
(3A6)16
=3×162＋10×161＋6×160
=(934)10

## Slide 30: 1.2 Number Conversion
(1) Conversion from Decimal to Binary
Integer part: divided by 2 to get the remainder until the quotient is 0.
Fractional part: multiplied by 2 to get integers until the fractional part is 0 (or the required precision is reached).
1.2.1 Conversion Between Binary and Decimal
Notes: Convert decimal number to binary number.
The integer part is divided by 2. Take the remainders.
The decimal part is multiplied by 2. Take the resulted integers.

## Slide 31
Example: (25.875)10＝(11001.111)2
25
Remainder
1 a0
0 a1
0 a2
1 a3
1 a4
12
6
3
1
0
2
2
2
2
2
Quotient
Notes: 25 is divided by 2. The 1st remainder is the lowest bit of the target number.
The last remainder is the highest bit of the target number.
The key point. 1 is less than 2. Now, the quotient is 0. The division ends.

## Slide 32
× 2 Integer
0.875
1.750 1 (a-1)
e.g. (25.875)10＝(11001.111)2
× 2
1.50 1 (a-2)
0.750
× 2
1.0 1 (a-3)
0.50
0.0

## Slide 33: Exercise

## Slide 34
(1) Conversion from Decimal to Binary
(179)10 =101100112
179÷2=89 Remainder 1
89÷2=44 1
44÷2=22 0
22÷2=11 0
11÷2=5 1
5÷2=2 1
2÷2=1 0
1÷2=0 1
higher bit
lower bit
When quotient is 0, stop!

## Slide 35
(2) Conversion from Binary to Decimal
How?
Calculate the weighted expansion of the binary number.
Example:
(11.1)2
=1×21＋1×20＋1×2-1 =(3.5)10

## Slide 36: Exercise

## Slide 37
(2) Conversion from Binary to Decimal
(10011)2
=1×24＋0×23＋0×22＋1×21＋1×20
=16+2+1=1910
(100010)2
=1×25＋0×24＋0×23＋0×22＋1×21＋0×20
=32+2=3410
(101.001)2
=1×22＋0×21＋1×20＋0×2-1＋0×2-2＋1×2-3
=4+1+1/8=5.12510

## Slide 38: 1.2.2 Conversion of Binary, Octal and Hexadecimal
(1) Conversion from Binary to Octal
Example: (1 011 101.011 010 1)2
=(135.324)8
From the radix point, put three bits in a group. Add 0 to the head or tail if the digits are inadequate to from a group.

## Slide 39
Example:
(101 1101.0110 101)2
=(5D.6A)16
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
From the radix point, put four bits in a group. Add 0 to the head or tail if the digits are inadequate to from a group.
(2) Conversion from Binary to Hexadecimal

## Slide 40
(3) Conversion from Octal to Binary
Example: (135.324)8
=(1 011 101.011 010 1)2
Replace each octal counting symbol with 3 bits.

## Slide 41
(4) Conversion from Hexadecimal to Binary
Replace each hex counting symbol with 4 bits.
Example:
(5D.6A)16
=(101 1101.0110 101)2
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111

## Slide 42: Exercise

## Slide 43
(1) Conversion from Binary to Octal
(100011001110)2
=(100 011 001 110)2
=43168
(11101101110101001)2
=(011 101 101 110 101 001)2
=3556518
(10.1011001011)2
=(010.101 100 101 100)2
=2.54548

## Slide 44
(2) Conversion from Binary to Hexadecimal
(100011001110)2
=(1000 1100 1110)2
=8CE16
(11101101110101001)2
=(0001 1101 1011 1010 1001)2
=1DBA916
(10.1011001011)2
=(0010.1011 0010 1100)2
=2.B2C16
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111

## Slide 45
(3) Conversion from Octal to Binary
(1357)8
=001 011 101 1112
= 1 011 101 1112
(2046.17)8
=010 000 100 110 . 001 1112
= 10 000 100 110 . 001 1112

## Slide 46
(4) Conversion from Hexadecimal to Binary
(BEAD)16
=1011 1110 1010 11012
(9F.46C)16
=1001 1111 . 0100 0110 11002
=1001 1111 . 0100 0110 112
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111

## Slide 47: 1.2.3 Conversion of Decimal, Octal and Hexadecimal
(1) Conversion from Decimal to Octal
Integer part: divided by 8 to get the remainder until the quotient is 0.
Fractional part: multiplied by 8 to get integers until the fractional part is 0 (or the required precision is reached).

## Slide 48
(2) Conversion from Decimal to Hexadecimal
Integer part: divided by 16 to get the remainder until the quotient is 0.
Fractional part: multiplied by 16 to get integers until the fractional part is 0 (or the required precision is reached).

## Slide 49
(3) Conversion from Octal to Decimal
How?
Calculate the weighted expansion of the octal number.

## Slide 50
(4) Conversion from Hexadecimal to Decimal
How?
Calculate the weighted expansion of the hex number.

## Slide 51
Example 1: (369)10=(561)8=(171)16
369
Remainder
1 a0
6 a1
5 a2
46
5
0
8
8
8
Quotient
369
Remainder
1 a0
7 a1
1 a2
23
1
0
16
16
16
Quotient

## Slide 52
Example 3: (171)16=(369)10
1×162+7×161+1×160=1×256+7×16+1=(369)10
Example 2: (561)8=(369)10
5×82+6×81+1×80=5×64+6×8+1=(369)10

## Slide 53: Exercise

## Slide 54
(1) Conversion from Hexadecimal to Decimal
(1CE8)16
=1×163+12×162+14×161+8×160
=740010
(F1A3)16
=15×163+1×162+10×161+3×160
=6185910
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111

## Slide 55
(2) Conversion from Octal to Decimal
(436.5)8
=4×82+3×81+6×80+5×8-1
=286.62510

## Slide 56
(467)10 =7238
467÷8=58 Remainder 3
58÷8=7 2
7÷8=0 7
(4) Conversion from Decimal to Octal
higher digit
lower digit
When quotient is 0, stop!

## Slide 57
(5) Conversion from Decimal to Hexadecimal
(3417)10 =D5916
3417÷16=213 9
213÷16=13 5
13÷16=0 13
D
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
higher digit
lower digit
When quotient is 0, stop!
Remainder

## Slide 58: Quiz

## Slide 59
Quiz
(10111011001)2
=010 111 011 0012=27318
(10111011001)2
=0101 1101 10012=5D916
(10111011001)2
=1×210+0×29+1×28+1×27+1×26+0×25+1×24+1×23+0×22+0×21+1×20
=1024+256+128+64+16+8+1
=149710
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
(10111011001)2(?)8(?)16(?)10

## Slide 60
(1234)8
=001 010 011 1002
(1234)8
=001 010 011 1002=0010 1001 11002
=29C16
(1234)8
=1×83+2×82+3×81+4×80
=1×512+2×64+3×8+4×1
=66810
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
(1234)8(?)2(?)16(?)10
Quiz

## Slide 61
(C0DE)16
=1100 0000 1101 11102
(C0DE)16
=1100 0000 1101 11102
=001 100 000 011 011 1102=1403368
(C0DE)16
=12×163+0×162+13×161+14×160
=12×4096+13×16+14×1
=4937410
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
(C0DE)16(?)2(?)8(?)10
Quiz

## Slide 62
(108)10=11011002
108÷2=54 0
54÷2=27 0
27÷2=13 1
13÷2=6 1
6÷2=3 0
3÷2=1 1
1÷2=0 1
(108)10  (?)2
higher bit
lower bit
When quotient is 0, stop!
Quiz
Remainder

## Slide 63
(108)10=1548
108÷8=13 4
13÷8=1 5
1÷8=0 1
(108)10  (?)8
higher digit
lower digit
When quotient is 0, stop!
Quiz
Remainder

## Slide 64
(108)10=6C16
108÷16=6 12
6÷16=0 6
C
10
11
12
13
14
15
A
B
C
D
E
F
1010
1011
1100
1101
1110
1111
(108)10  (?)16
higher digit
lower digit
When quotient is 0, stop!
Quiz
Remainder

## Slide 65: 1.3 Signed Binary Number
Signed-Magnitude
The Ones’ Complement
The Two’s Complement

## Slide 66: 1.3.1 Signed-Magnitude
Positive number: ＋10011  [010011]SM
Negative number: －10011  [110011]SM
The Signed-Magnitude of the positive number is itself. Just put a ‘0’in leftmost direction.
(2)The Signed-Magnitude of the negative number is to
put a ‘1’in leftmost direction.

## Slide 67: 1.3.2 Ones’ Complement
Positive number: X1＝＋1001  [01001]OC
Negative number: X2＝－1001  [10110]OC
The Ones’ Complement of the positive number is itself. Just put a ‘0’in leftmost direction.
The Ones’ Complement of the negative number is to put a ‘1’in leftmost direction, and reverse ‘0’ and ‘1’.

## Slide 68
Example: Calculate the Ones’ Complement of
- 1101100.
11111111
- 1101100
10010011
The Ones’ Complement: 10010011
Why named the ones’ complement?
The ones’ complement:
Subtract the absolute value of negative number from all bits of “1” (111…111).

## Slide 69
Example:
The Ones’ Complement of －10101 is 101010
111111
10101
101010

## Slide 70
Example:
The Ones’ Complement of －0.101 is 1.010
1.111
0.101
1.010

## Slide 71: 1.3.3 Two’s Complement
Positive number: X1＝＋10011  [010011]TC
Negative number: X2＝－01010  [110110]TC
The Two’s Complement of the positive number is itself. Just put a ‘0’in leftmost direction.
The Two’s Complement of the negative number is to put a ‘1’ in leftmost direction, reverse ‘0’ and ‘1’, and add ‘1’ to the tail.

## Slide 72
The Two’s Complement of －10101 is 101011
Why named the two’s complement?
The two’s complement:
Subtract the absolute value from 1 with all bits of “0” (1000…000=2n).
1000000
－ 10101
101011
11111
borrow bits

## Slide 73
The Two’s Complement of －0.1010 is:
10－0.1010＝1.0110
10.0000
－ 0.1010
1.0110
1 11
borrow bits

## Slide 74: 1.4 Addition and Subtraction of Signed Binary Numbers
0.1000
－0.0011
0.1011
Calculate X1＋X2 and X1－X2
e.g. X1＝－0.0011 X2＝＋0.1011
X1＋X2＝[0.1000]SM
1. Addition and Subtraction of Signed-Magnitude
X1＋X2=－0.0011＋0.1011
Subtract the absolute value, and the result is positive.
Solution

## Slide 75
X1－X2 ＝[1.1110]SM
0.1110
＋0.1011
0.0011
(2)X1－X2＝[－0.0011]－[0.1011]
Add the absolute value, and the result is negative.
＝－[0.0011 ＋ 0.1011]

## Slide 76
[X1＋X2]OC＝[X1]OC ＋[X2]OC
[X1－X2]OC ＝[X1]OC＋[－X2]OC
2. Addition and Subtraction of One’s Complement
If the sign bit has a carry, the carry should be added to the lowest bit of the sum result, named as end-around carry.

## Slide 77
e.g. X1＝0.1100 X2＝0.0010
Calculate [X1＋X2]OC and [X1－X2]OC
(1) [X1＋X2]OC＝[X1]OC ＋[X2]OC
＝0.1100＋0.0010＝[0.1110]OC
0.1100
+ 0.0010
0.1110
Solution

## Slide 78
0.1100
+ 1.1101
[1]0.1001
1
0.1010
＝ 0.1100＋1.1101
＝ 10.1001
＝ [0.1010]OC
[X1－X2]OC＝[X1]OC ＋[－X2]OC
(2) X1＝0.1100 X2＝0.0010
End-Around Carry
11 1
carry bits

## Slide 79
3. Addition and Subtraction of Two’s Complement
[X1＋X2]TC＝[X1]TC＋[X2]TC
[X1－X2]TC＝[X1]TC＋[－X2]TC
Calculate the Two's Complement of each number, and do addition.
Drop the carry on the sign bit.

## Slide 80
e.g. X1＝－0.1100 X2=－0.0010
Calculate [X1＋X2]TC and [X1－X2]TC
(1)[X1＋X2]TC＝[X1]TC＋[X2]TC
＝1.0100＋1.1110＝[1.0010]TC
1.0100
+ 1.1110
[1]1.0010
Solution
11 1
carry bits

## Slide 81
[X1－X2]TC＝[X1]TC ＋[－X2]TC
＝1.0100＋0.0010＝[1.0110]TC
1.0100
+ 0.0010
1.0110
(2) X1＝－0.1100 X2=－0.0010

## Slide 82
[X1+X2]TC＝[X1]TC＋[X2]TC＝？？？
Example 1: X1＝+15 X2=-5
    Overflow of Addition in Two’s Complement
Example 2: X1＝+0111 X2=+0011
11111111
00001111（15）
+11111011（-5）
00001010（10）
0111
0111（7）
+0011（3）
1010（-6）
00111
00111（7）
+00011（3）
01010（10）
Overflow: the higher two carry bits are different.
Solution: Add one more bit in Two’s Complement.

## Slide 83: Multiplication & Division
Multiplication: shifted addition
Division: shifted subtraction
11
× 10
00
11
110
110
10
11
10
10
10
0
11×10=110
110÷10=11

## Slide 84: 1.5.1 Binary Coded Decimal
1.5 Numerical Codes
1.5.2 Gray Code
1.5.3 Parity Code

## Slide 85: 1.5.1 Binary Coded Decimal
Binary Coded Decimal (BCD):
Decimal
Number
0 0000 0011 0000
1 0001 0100 0001
2 0010 0101 0010
3 0011 0110 0011
4 0100 0111 0100
5 0101 1000 1000
Excess-3
Code
8421
Code
5421
Code
6 0110 1001 1001
7 0111 1010 1010
8 1000 1011 1011
9 1001 1100 1100

## Slide 86: 1.5.1 Binary Coded Decimal
Binary Coded Decimal (BCD):
Decimal
Number
0 0000 0011 0000
1 0001 0100 0001
2 0010 0101 0010
3 0011 0110 0011
4 0100 0111 0100
5 0101 1000 1000
Excess-3
Code
8421
Code
5421
Code
6 0110 1001 1001
7 0111 1010 1010
8 1000 1011 1011
9 1001 1100 1100

## Slide 87: 1.5.1 Binary Coded Decimal
Binary Coded Decimal (BCD):
Decimal
Number
0 0000 0011 0000
1 0001 0100 0001
2 0010 0101 0010
3 0011 0110 0011
4 0100 0111 0100
5 0101 1000 1000
Excess-3
Code
8421
Code
5421
Code
6 0110 1001 1001
7 0111 1010 1010
8 1000 1011 1011
9 1001 1100 1100

## Slide 88: 1.5.1 Binary Coded Decimal
Binary Coded Decimal (BCD):
Decimal
Number
0 0000 0011 0000
1 0001 0100 0001
2 0010 0101 0010
3 0011 0110 0011
4 0100 0111 0100
5 0101 1000 1000
Excess-3
Code
8421
Code
5421
Code
6 0110 1001 1001
7 0111 1010 1010
8 1000 1011 1011
9 1001 1100 1100

## Slide 89
1. 8421 Code
The weights are 8－4－2－1.
1010～1111 are invalid codes.
2168 0010 0001 0110 1000
Example: Convert the Decimal number to 8421 Code

## Slide 90
2. Excess-3 Code
3. 5421 Code
Each code is formed by adding 0011 to the 8421 Code.
The weights are 5－4－2－1.

## Slide 91: 1.5.2 Gray Code
Gray Code (reflected binary code)
0 0000
1 0001
8 1100
9 1101
10 1111
11 1110
12 1010
13 1011
14 1001
15 1000
2 0011
3 0010
4 0110
5 0111
6 0101
7 0100
Decimal Gray Code Decimal Gray Code

## Slide 92
2 bits: 00, 01, 11, 10
Reflected: 10, 11, 01, 00
Connected: 00, 01, 11, 10, 10, 11, 01, 00
Add 0: 000, 001, 011, 010, 10, 11, 01, 00
Add 1: 000, 001, 011, 010,110, 111, 101, 100
The Generation of 3-bit Gray Code

## Slide 93: 1.5.3 Parity Code
Add a check bit to the data.
If the number of ones is odd in the whole code, it is named as Odd Parity.
If the number of ones is even in the whole code, it is named as Even Parity.

## Slide 94
Decimal
Odd Parity
0 0000 1
1 0001 0
2 0010 0
3 0011 1
4 0100 0
5 0101 1
6 0110 1
7 0111 0
8 1000 0
9 1001 1
Data
Check Bit
Number of ones
1
1
1
3
1
3
3
3
1
3

## Slide 95
Decimal
Even Parity
0 0000 0
1 0001 1
2 0010 1
3 0011 0
4 0100 1
5 0101 0
6 0110 0
7 0111 1
8 1000 1
9 1001 0
Data
Check Bit
Number of ones
0
2
2
2
2
2
2
4
2
2