## Slide 1: Chapter 3 Digital Circuit
3.1 CMOS Transistor
3.2 CMOS Gate
3.3 Electrical Characteristics

## Slide 2: 3.1 CMOS Transistor
1 (High-state)
0 (Low-state)
5.0V
3.5V
1.5V
0.0V
Logic Level of 5V

## Slide 3
Gate = “0”
NMOS transistor is OFF.
Gate = “1” (high-state)
NMOS transistor is ON.
drain
source
gate
+
Vgs
NMOS Transistor

## Slide 4
Gate = “1”
PMOS transistor is OFF.
Gate = “0” (low-state)
PMOS transistor is ON.
PMOS Transistor
source
drain
gate
+
Vgs

## Slide 5: 3.2 CMOS Gate
CMOS Inverter
COMS NAND Gate
COMS NOR Gate
CMOS AND-OR-Inverter
CMOS Buffer
Three-State Buffer
Transmission Gate
Schmitt-Trigger Inverter
Open-Drain Output Circuit
Wired Logic

## Slide 6
1. VIN = 0.0V
  Tn is OFF
  Tp is ON
  VOUT  VDD = 5.0V
2. VIN = VDD = 5.0V
  Tn is ON
  Tp is OFF
  VOUT  0V
VDD = +5.0V
VOUT
VIN
Tp
Tn
G
D
S
S
pmos
nmos
CMOS Inverter
VOUT = VIN

## Slide 7
VDD = +5.0V
Vout
Vin
Tp
Tn
VDD
A
Z
Vin | Vout
Low | High
High | Low
CMOS Inverter

## Slide 8
  1. A or B is low-state
  T1 or T3 is OFF
  T2 or T4 is ON
  Z  VDD
  2. A and B are high-state
  T1 and T3 are ON
  T2 and T4 are OFF
  Z  0V
VDD = +5.0V
Z
A
B
T1
T2
T4
T3
Z = A·B
CMOS NAND Gate

## Slide 9
1. A and B are low-state
T1 and T3 are OFF
T2 and T4 are ON
Z  VDD
2. A or B is high-state
T1 or T3 is ON
T2 or T4 is OFF
Z  0V
VDD = +5.0V
Z
A
B
T1
T2
T4
T3
Z = A+B
CMOS NOR Gate

## Slide 10
VDD = +5.0V
A
B
Z
C
D
Z = A·B + C·D
A
B
C
D
z
Q1
Q2
Q3
Q4
Q6
Q5
Q7
Q8
(1) Q1 and Q3 are ON,
or
(2) Q5 and Q7 are ON,
Z is 0V.
Otherwise, Z is high-state.
CMOS AND-OR-Inverter

## Slide 11
VDD = +5.0V
A
Z
CMOS Buffer

## Slide 12: Three-state Buffer
EN=0,
C=1, Tp is OFF
B=1, D=0, Tn is OFF
OUT is floating state
high-impedance disconnected state
EN=1,
C=A , B=0 , D=A
OUT=A
OUT is low-state or high-state
VCC
OUT
EN
A
B
C
D
Tp
Tn
A
EN
OUT

## Slide 13: Transmission Gate
EN = 0，EN_L = 1，
Gate is OFF，
A and B are disconnected
EN = 1，EN_L = 0，
Gate is ON，
bidirectional transmission
A=B
EN
EN_L
A
B

## Slide 14: Schmitt-Trigger Inverter
VOUT
VIN
5.0
2.1
2.9
5.0
VT+
VT-
Input rises to 2.9V, output becomes low-state.
Input falls to 2.1V, output becomes high-state.
input
threshold
VT+
VT-
Hysteresis 2.9V-2.1V=0.8V
2.1V
2.9V

## Slide 15: Open-Drain Output Circuit
A
B
Z
VCC
VCC
’
A
B
Z
NAND Gate
The drain terminal is not connected to the voltage directly.

## Slide 16: Wired Logic
A
B
Z
VCC
VCC
R
C
D
VCC
Z1
Z2
Wired
logic
Z = Z1 · Z2
= A·B · C·D
= A·B · C·D
= A·B + C·D

## Slide 17: Unused inputs of CMOS circuit
X
Z
1k
+5V
X
Z
X
Z

## Slide 18
(1) Logic Level
(2) Fanin
(3) Fanout
(4) Direct Current Noise Margin
(5) Transition Time
(6) Propagation Delay
(7) Diode
(8) Bipolar junction transistor
3.3 Electrical Characteristics

## Slide 19
High State
Low State
VCC
70%VCC
30%VCC
0
VOLmax:Ground+0.1V
VILmax:
VIHmin:
VOHmin:Vcc-0.1V
Logic Level

## Slide 20: Fanin
For a logic gate, the number of inputs allowed is named as “fanin”.
NOR gate ≤4
NAND gate ≤6

## Slide 21: Fanout
“Fanout” is the number of gates that a logic gate can drive.

## Slide 22
74HCT drives 74LS
High-stat fanout：
Overall fanout：min(200,10)=10
CMOS: 74HCT
IOH = 4 mA
IOL = 4 mA
IIH = 1 A
IIL = 1 A
TTL: 74LS
IOH = 0.4mA
IOL = 8 mA
IIH = 0.02mA
IIL = 0.4 mA
Low-state fanout：
Fanout

## Slide 23
Residual driving capacity：
CMOS: 74HCT
IOH = 4 mA
IOL = 4 mA
IIH = 1 A
IIL = 1 A
TTL: 74LS
IOH = 0.4mA
IOL = 8 mA
IIH = 0.02mA
IIL = 0.4 mA
74HCT drives 74LS
Fanout

## Slide 24
When two logic gates are cascaded, we use the “direct current noise margin” to measure the noise voltage gap between the driving gate and the driven gate.
If the DC noise margin is positive, the voltage level of both the driving gate and the driven gate are compatible.
Otherwise, the voltage level of the driving gate is destroyed and unrecognizable for the driven gate.
Direct Current Noise Margin

## Slide 25
VOLmax
0.5
VOHmin
2.7
VIHmin
2.0
VILmax
0.8
TTL
VOLmax
0.33
VILmax
0.8
VIHmin
2.0
VOHmin
3.84
CMOS
  Low state: VILmax-VOLmax
  High state: VOHmin-VIHmin
Direct Current Noise Margin

## Slide 26
74HCT drives 74LS
High state: 3.84 – 2.0 = 1.84V
Low state: 0.8 – 0.33 = 0.47V
VOLmax
0.33
VILmax
0.8
VIHmin
2.0
VOHmin
3.84
74HCT
VOLmax
0.5
VOHmin
2.7
VIHmin
2.0
VILmax
0.8
74LS
74LS drives 74HCT
High state: 2.7 – 2.0 = 0.7V
Low state: 0.8 – 0.5 = 0.3V
Therefore, they are compatible.

## Slide 27
10%
10%
rise time tr
Fall time tf
In the digital circuit, the time required for the circuit output to change between the low-state and high-state voltage is named as the “transition time”.
Transition Time
circuit output from low-state to high-state
circuit output from high-state to low-state

## Slide 28
VIN
VOUT
When the voltage level of the circuit input changes, and the voltage level of the circuit output changes correspondingly, the total time required is named as the “propagation delay”.
Propagation Delay
The input changes to be high, and the output changes to be low
The input changes to be low, and the output changes to be high

## Slide 29
＋
Diode
Anode
Cathode
+
Rf
Vd
forward-biased
voltage level of anode is higher than that of cathode
+
reverse-biased
voltage level of anode is lower than that of cathode

## Slide 30
A
B
D1
D2
R
VCC 5V
Y
Input (5V, 5V), output ≈ 5V
Input (0V, 5V), output = 0.6V
diode-drop 0.6V
Diode

## Slide 31: Bipolar junction transistor
base
collector
emitter
VCC
vo
+
-
vi
+
-
RB
RC
iC
NPN Transistor
NPN Transistor Inverter
if the voltage level of “base” is high, the NPN transistor is conductive.
Otherwise, the NPN transistor is not conductive.