## Slide 1: Chapter 7 Verilog Implementation of Logic Circuit
7.1 Verilog Implementation of Logic Gates
7.2 Verilog Implementation of Combinational Logic Circuit
7.3 Verilog Implementation of Flip-Flop
7.4 Verilog Implementation of Synchronous Sequential Logic Circuit

## Slide 2
Essential Questions About Verilog Grammar

## Slide 3
Is the Verilog identifier case-sensitive?
Yes, “A” and “a” are different.

## Slide 4
What is the first character of the identifier of Verilog?
Letter (“A”, “a”, “c”, …)
Underline (“_”)

## Slide 5
What is the identifier composed of ?
Letter (“A”, “a”, “c”, …)
Underline (“_”)
Number (“1”, “2”, “3”, …)
“$” Sign

## Slide 6
Which sign did you put to specify the end of each statement in Verilog?
Semicolon ( “ ; ” )

## Slide 7
Z: High resistance (when it is an open circuit)
X: Unknown value (without initialization)
What are the special values of variables in Verilog?

## Slide 8
wire: commonly used in the combinational logic circuit (like a wire connection)
reg: commonly used in the sequential logic circuit (like a register)
What are the most commonly used variable types in Verilog?

## Slide 9
wire: by default
What is the variable type if you forget to define it?

## Slide 10
Yes, the output variable always comes first in the built-in logic gates.
Is there a priority of parameter order in the built-in logic gates of Verilog?
But for the module, you can put the variables in any order.
not U3 (F,A);
F
A
module NOT_G (A, F);

## Slide 11
How to define numbers in Verilog?
2’b00: 2-bit binary number “00”
6’o00: 6-bit octal number “000 000”
8’h00: 8-bit hexadecimal number “0000 0000”
3’d0: 3-bit decimal number “000”

## Slide 12
How to define the signed number in Verilog?
3’sb101: 3-bit signed binary number “101”
The Two’s Complement: [101]TC
The Signed Magnitude: [111]SM
The True Value: [−11]2
[−3]10
101110111

## Slide 13
input [3:0] A, B;
How to define the bit width of variables in Verilog?
A are B are both 4-bit wire type input variables.

## Slide 14: 7.1 Verilog Implementation of Logic Gates
(1) AND Gate
(2) OR Gate
(3) NOT Gate
(4) NAND Gate
(5) NOR Gate
(6) Buffer
(7) AND-OR-Inverter

## Slide 15
AND gate
module AND_G(A, B, F);
input A, B;
output F;
and U1(F, A, B);
endmodule
Gate level
description
Dataflow level
description
module AND_G (A,B,F);
input A,B;
output F;
assign F=A&B；
endmodule
B
F
A

## Slide 16
module OR_G (A,B,F);
input A,B;
output F;
or U2 (F,A,B);
endmodule
module OR_G (A,B,F);
input A,B;
output F;
assign F=A|B；
endmodule
B
F
A
OR gate
Gate level
description
Dataflow level
description

## Slide 17
module NOT_G (A,F);
input A;
output F;
not U3 (F,A);
endmodule
module NOT_G (A,F);
input A;
output F;
assign F=~A;
endmodule
F
A
NOT gate
Gate level
description
Dataflow level
description

## Slide 18
module NAND_G(A,B,F);
input A,B;
output F;
nand U4(F,A,B);
endmodule
module NAND_G(A,B,F);
input A,B;
output F;
assign F= ~(A & B);
endmodule
B
F
A
NAND gate
Gate level
description
Dataflow level
description

## Slide 19
module NOR_G (A,B,F);
input A,B;
output F;
nor U5 (F,A,B);
endmodule
module NOR_G (A,B,F);
input A,B;
output F;
assign F= ~(A | B);
endmodule
B
F
A
NOR gate
Gate level
description
Dataflow level
description

## Slide 20
module BUF_G (A,F);
input A;
output F;
buf U6 (F,A);
endmodule
module BUF_G (A,F);
input A;
output F;
assign F=A;
endmodule
F
A
Buffer
Gate level
description
Dataflow level
description

## Slide 21
module ANDORNOT_G(A, B, C, D, F);
input A, B, C, D;
output F;
wire AandB, CandD;
and U1(AandB, A, B);
and U2(CandD, C, D);
nor U3(F, AandB, CandD);
endmodule
A
B
C
D
F
AND-OR-Inverter
Gate level
description

## Slide 22
module ANDORNOT_G(A, B, C, D, F);
input A, B, C, D;
output F;
assign F = ~ ((A&B)|(C&D));
endmodule
Dataflow level description
A
B
C
D
F
AND-OR-Inverter

## Slide 23: 7.2 Verilog Implementation of Combinational Logic Circuit
(1) 4-to-1 Line Data Selector
(2) 4-Bit Numerical Comparator
(3) 8-3 Encoder
(4) 3-8 Decoder

## Slide 24
module MUX4_1(Y,D0,D1,D2,
input D0,D1,D2,D3;
output Y;
input A0,A1;
endmodule
assign Y=((~A1)&(~A0)&D0)|((~A1)&A0&D1)
|(A1&(~A0)&D2)|(A1&A0&D3);
D3,A0,A1);
Dataflow level description
4-to-1 Line Data Selector

## Slide 25
module MUX4_1(Y,D0,D1,D2,D3,A0,A1);
input D0,D1,D2,D3;
output Y;
input A0,A1;
endmodule
not U1(A0n,A0);
wire A0n,A1n,and1,and2,and3,and4;
and U3(and1,A1n,A0n,D0);
not U2(A1n,A1);
and U4(and2,A1n,A0,D1);
and U5(and3,A1,A0n,D2);
and U6(and4,A1,A0,D3);
or U7(Y,and1,and2,and3,and4);
Gate level description

## Slide 26
2’b01: Y=D1;
case (A)
2’b00: Y=D0;
endmodule
2’b11: Y=D3;
2’b10: Y=D2;
endcase
module MUX4_1(Y,D0,D1,D2,D3,A);
input D0,D1,D2,D3;
output reg Y;
input [1:0] A;
always@(D0 or D1 or D2 or D3 or A)
Use “case” statement
Behavior level description

## Slide 27
Use “if_else” statement
if (A==2’b00) Y=D0;
else if(A==2’b01) Y=D1;
endmodule
else Y=D3;
else if(A==2’b10) Y=D2;
module MUX4_1(Y,D0,D1,D2,D3,A);
input D0,D1,D2,D3;
output reg Y;
input [1:0] A;
always@(D0 or D1 or D2 or D3 or A)
Behavior level description

## Slide 28
module COMP(A, B, LG, EQ, SM);
input [3:0] A, B;
output reg LG, EQ, SM;
always @(A or B)
if (A > B)
begin
LG = 1;
EQ = 0;
SM = 0;
end
else if (A == B)
begin
LG = 0;
EQ = 1;
SM = 0;
end
else
begin
LG = 0;
EQ = 0;
SM = 1;
end
endmodule
Behavior level description
4-Bit Numerical Comparator

## Slide 29
module ENC8_3(I, Y);
input [7:0] I;
output reg [2:0] Y;
always @(I)
case (I)
8’b11111110: Y = 3’b000;
8’b11111101: Y = 3’b001;
8’b11111011: Y = 3’b010;
8’b11110111: Y = 3’b011;
8’b11101111: Y = 3’b100;
8’b11011111: Y = 3’b101;
8’b10111111: Y = 3’b110;
8’b01111111: Y = 3’b111;
endcase
endmodule
Behavior level
description
8-3 Encoder

## Slide 30
module DEC3_8(IN, OUT);
input [2:0] IN;
output reg [7:0] OUT;
always @(IN)
case (IN)
3’b000: OUT = 8’b11111110;
3’b001: OUT = 8’b11111101;
3’b010: OUT = 8’b11111011;
3’b011: OUT = 8’b11110111;
3’b100: OUT = 8’b11101111;
3’b101: OUT = 8’b11011111;
3’b110: OUT = 8’b10111111;
3’b111: OUT = 8’b01111111;
endcase
endmodule
Behavior level
description
3-8 Encoder

## Slide 31: 7.3 Verilog Implementation of Flip-Flop
(1) Rising-Edge Triggered D Flip-Flop
(2) Integrated D Flip-Flop
(3) Falling-Edge Triggered J-K Flip-Flop
(4) Integrated J-K Flip-Flop

## Slide 32
module D_ff (D, CLK, Q, Qn);
input D, CLK;
output reg Q, Qn;
always @(posedge CLK)
begin
Q <= D;
Qn <= ~D;
end
endmodule
Rising-Edge Triggered D Flip-Flop

## Slide 33
module D_Int_ff (D, CLK, Q, Qn, Set, Reset);
input D, CLK, Set, Reset;
output reg Q, Qn;
always @(posedge CLK or negedge Reset or negedge Set)
if (!Set)
begin
Q <= 1’b1;
Qn <=1’b0;
end
else if (!Reset)
begin
Q <= 1’b0;
Qn <= 1’b1;
end
else
begin
Q <= D;
Qn <= ~D;
end
endmodule
Integrated D Flip-Flop

## Slide 34
module JK_ff (J, K, CLK, Q, Qn);
input J, K, CLK;
output Q, Qn;
reg Q;
assign Qn = ~Q;
always @(negedge CLK)
case ({J, K})
2’b00: Q <= Q;
2’b01: Q <= 0;
2’b10: Q <= 1;
2’b11: Q <= ~Q;
endcase
endmodule
Falling-Edge Triggered J-K Flip-Flop

## Slide 35
module JK_Int_ff (J, K, CLK, Q, Qn, Set, Reset);
input J, K, CLK, Set, Reset;
output Q, Qn;
reg Q;
assign Qn = ~Q;
always @(negedge CLK or negedge Reset or negedge Set)
if (!Set)
Q <= 1;
else if (!Reset)
Q <= 0;
else
case ({J, K})
2’b00: Q <= Q;
2’b01: Q <= 0;
2’b10: Q <= 1;
2’b11: Q <= ~Q;
endcase
endmodule
Integrated J-K Flip-Flop

## Slide 36: 7.4 Verilog Implementation of Synchronous Sequential Circuit
(1) 3-Bit Left Shift Register
(2) 4-Bit Binary Addition Counter
(3) Sequence Detector of Binary Numbers “111”

## Slide 37
module left_shifter(x, CP, Q);
input x, CP;
output reg [2:0] Q;
always @(negedge CP)
begin
Q = Q << 1;
Q[0] = x;
end
endmodule
3-Bit Left Shift Register

## Slide 38
module left_shifter_clr(x, CP, clr, Q);
input x, CP, clr;
output reg [2:0] Q;
always @(posedge CP or negedge clr)
if (!clr)
Q = 3’b000;
else
begin
Q = Q << 1;
Q[0] = x;
end
endmodule
3-Bit Left Shift Register with Input “Reset”

## Slide 39
module counter(D, CLK, CR, LD, CTt, CTp, Q);
input [3:0] D;
input CLK, CR, LD, CTt, CTp;
output reg [3:0] Q;
always @(posedge CLK or negedge CR)
if (!CR)
Q = 0;
else if (!LD)
Q = D;
else if (CTt = =1 && CTp = =1)
Q = Q+1;
else
Q = Q;
endmodule
4-Bit Binary Addition Counter

## Slide 40
module seqdet(datain, clk, reset, dataout);
input datain, clk, reset;
output dataout;
reg [1:0] state_reg,
state_next;
localparam A = 2’b00,
B = 2’b01,
C = 2’b10;
assign dataout = (state_reg = = C && datain = = 1’b1)? 1’b1 : 1’b0;
always @(negedge clk or negedge reset)
if (!reset)
state_reg <= A;
else
state_reg <= state_next;
Sequence Detector of Binary Numbers “111”

## Slide 41
always @(state_reg or datain)
case (state_reg)
A: if (datain = = 1’b0)
state_next = A;
else state_next = B;
B: if (datain = = 1’b0)
state_next = A;
else state_next = C;
C: if (datain = = 1’b0)
state_next = A;
else state_next = C;
default: state_next = A;
endcase
endmodule